# ESP32 + Display TFT 1.4 240x240
- https://arduino-er.blogspot.com/2020/07/esp32-13-inch-240x240-ips-lcd-st7789.html
- https://www.youtube.com/watch?v=PUV9_OdMcCA
- 7 pins are used to connect to MCU:

  # Pin Label Description
  1 GND LCD Power ground
  2 VCC LCD power supply is positive (3.3V)
  3 SCL LCD SPI bus clock signal - connect to ESP32 18 TFT_SCLK
  4 SDA LCD SPI bus write data signal - connect to ESP32 23 TFT_MOSI
  5 RES LCD reset control signal(Low level reset) - connect to ESP32 4 TFT_RST
  6 DC LCD register/data - connect to EST32 2 TFT_DC
  7 BLK LCD backlight control signal - Connect to 3.3V
Librería - https://github.com/Bodmer/TFT_eSPI/wiki/Installing-on-PlatformIO